Next generation motor record
Torsten Bögershausen
Motion Control and Automation Group
www.europeanspallationsource.se

---
Situation at ESS
- Still early phase, at least for instruments
- Focus on EherCAT based HW
- 2 Software platforms:
  - Beckhoff TwinCAT (commercial)
  - ECMC (”open source”)

---
Axis Record
- Intention/purpose:
  - Fix bugs
  - Implement features we need
  - Independent code base
   call it axis rather than motor
- Follow up in 2018 @ APS

---
Situation at ESS -2
- EPICS conferences: collect motioneers face
  to face
- ”Servo motors in focus”, microstepping, closed loop
- Deadbands needed
  Matt Person tech-talk (SDBD, RTRY and RDBD)

---
Commissioning
- How do you commission the controller?
  Vendor specific tool ?
  Motor Record ?
- Where do you store the low-level configuration ?
  Central DB
  FileSystem
  Laptop
- Where is the ”truth” ?

---
Parameters in motorRecord
- Can configure a stepper quite well:
  SREV/UREV or MRES
  VELO, VMAX, ACCL, RDBD, DLY, SDBD
  DLLM, DLLM
  JVEL, JAR, HVEL
- And even
  PID

---
Parameters in controller
- Scaling, dynamics, soft limits
  SREV/UREV
  VELO, VMAX, ACCL, JERK, RDBD, DLY, SDBD
  DLLM, DLLM, JVEL, JAR
- Homing parameters
- Encoders allow better dynamics
- Lots of (optional) dynamic parameters

---
Vendor tool
- Modern controller: Must use an engineering tool:
  TwinCAT, DeltaTau, IcePAP...
- Parameters: Motor&Encoder resolution
  type of encoder
  PID, FF, Deadbands, Monitors
  (following, acc, position, current overtrip), homing procedures
- Own soft limits outside MR

---
Who knows what ?
- Beamline users (EPICS)
- Instrument scientist (EPICS)
- Control engineers (EPICS)
- Motion control enginees (vendor tool)

---
Where is the truth ?
3 levels:
- Beamline users
- Control engineers (EPICS)
- Experts (e.g. instrument scientist)
- Motion control engineers
#Driver reads contoller:
out=HLenabled?;Hlvalue?
in=1;169 CHLM_En=1 CHLM=169
#Record gets value from driver:
motorRecord.cc:3943 IOC:m1 pmr->dhlm=169 maxValue=169

---
motor record @ ESS

---
Solved headaches
- Configuration: sync controller 20-50
  Record: 5-10 (e.g. VMAX, LLM)
- HOMF when on a limit switch

---
Improvements 1
- State machine, dev support, model 3 driver:
  move(), moveVelocity(), home(), stop()
- Record today:
  doStartMoving()
  doStartJogging()
  doStartHoming()
  devSupStop()

---
Improvements 2
- Done: RMP: 32 bit not enough, float64 better
  Why specifies motorRecord.html ”double”
- Done in axis:
  Generate field documentation from dbd
  (axisRecord.dbd.pod)

---
Added fields
MISV: MISS alarm serVerity
SDBD: Set point DeadBand
MFLG: Flags from driver
PRIV: Private data (last, info from driver)
In model 3 driver:
-MsgTxt

---
Removed fields
LVAL, LDVL, LRVL
ALST, MLST
FRAC (not removed, but no function)

---
Automated tests
- Find many bugs
- Python based
- With real hardware
- With a dedicated simulator
- Set up a test Db
- Allow refactoring

---
Upgrade, Migration
- We (at ESS) converted into axis good - but:
  Lost connection to comunity.
  Lost soft motor
- Re-done all changes inside ”motor”:
  motor 6.92
- Device support still old, but isolated:
  motorDevSup.c

---
That's it
Thanks for listening